SHIP/SHORE SAFETY CHECK LIST

Ship's Name:

Berth:

Port:

Date of Arrival:

Time of Arrival:

INSTRUCTIONS FOR COMPLETION:

The safety of operations requires that all questions should be answered affirmatively by clearly ticking (V) the appropriate box. If an affirmative answer is not possible, the reason should be given and agreement reached upon appropriate precautions to be taken between the ship and the terminal. Where any question is considered to be not applicable, then a note to that effect should be inserted in the remarks column.

A box in the columns «Ship» and «Terminal» indicates that checks shall be carried out by the party concerned.

The presence of the letters A, P or R in the column «Code» indicates the following:

A - any procedures and agreements should be in writing in the remarks column of this check list or other mutually acceptable form.

In either case, the signature of both parties should be required.

P - in the case of a negative answer the operation should not be carried out without the permission of the port authority.

R - indicates items to be re-checked at intervals not exceeding that agreed in the declaration.

PART'A'- BULK LIQUID GENERAL

(This reproduction of Part A excludes questions 37/46 covering Crude Oil Washing and Inert Gas Systems)

|  | General | Ship | Terminal | Code | Remarks |
| --- | --- | --- | --- | --- | --- |
| 1. | Is the ship securely moored? |  |  | R | *** |
| 2. | Are emergency towing wires correctly positioned? |  |  | R |  |
| 3. | Is there safe access between ship and shore? |  |  | R |  |
| 4. | Is the ship ready to move under its own power? |  |  | PR |  |
| 5. | Is there an effective deck watch in attendance on board and adequate supervision on the terminal and on the ship? |  |  | R |  |
| 6. | Is the agreed ship/shore communication system operative? |  |  | AR |  |
| 7. | Has the emergency signal to be used by the ship and shore been explained and understood? |  |  | A |  |
| 8. | Have the procedures for cargo, bunker and ballast handling been agreed? |  |  | AR |  |
| 9. | Have the hazards associated with toxic substances in the cargo being handled been identified and understood? |  |  |  |  |
| 10. | Has the emergency shutdown procedure been agreed? |  |  | A |  |
| 11. | Are fire hoses and fire-fighting equipment on board and ashore positioned and ready for immediate use? |  |  | R |  |
| 12. | Are cargo and bunker hoses/arms in good condition, properly rigged and appropriate for the service intended? |  |  |  |  |
| 13. | Are scuppers effectively plugged and drip trays in position, both on board and ashore? |  |  | R |  |
| 14. | Are unused cargo and bunker connections properly secured with blank flanges fully bolted? |  |  |  |  |
| 15. | Are sea and overboard discharge valves, when not in use, closed and visibly secured? |  |  |  |  |
| 16. | Are all cargo and bunker tank lids closed? |  |  |  |  |
| 17. | Is the agreed tank venting system being used? |  |  | AR |  |

*	Stop cargo at:........... kts wind vel.

*	Disconnect at:.......... kts wind vel.

*	Unberth at:............ kts wind vel.

PART 'A' - BULK LIQUID GENERAL (continued)

(This reproduction of Part A excludes questions 37/46 covering Crude Oil Washing and Inert Gas Systems)

| General | Ship | Terminal | Code | Remarks |
| --- | --- | --- | --- | --- |
| 18. | Has the operation of the P/V valves and/or high velocity vents been verified using the checklift facility, where fitted? |  |  |  |  |
| 19. | Are hand torches of an approved type? |  |  |  |  |
| 20. | Are portable VHF/UHF transceivers of anapproved type? |  |  |  |  |
| 21. | Are the ship's main radio transmitter aerials earthed and radars switched off? |  |  |  |  |
| 22. | Are electric cables to portable electrical equipment disconnected from power? |  |  |  |  |
| 23. | Are all external doors and ports in the accommodation closed? |  |  | R |  |
| 24. | Are window-type air conditioning units disconnected? |  |  |  |  |
| 25. | Are air conditioning intakes which may permit the entry of cargo vapours closed? |  |  |  |  |
| 26. | Are the requirements for the use of galley equipment and other cooking appliances being observed? |  |  | R |  |
| 27. | Are smoking regulations being observed? |  |  | R |  |
| 28. | Are naked light regulations being observed? |  |  | R |  |
| 29. | Is there provision for an emergency escape? |  |  |  |  |
| 30. | Are sufficient personnel on board and ashore to deal with an emergency? |  |  | R |  |
| 31. | Are adequate insulating means in place in the ship/shore connection? |  |  |  |  |
| 32. | Have measures been taken to ensure sufficient pumproom ventilation? |  |  | R |  |
| 33. | If the ship is capable of closed loading, have the requirements for closed operations been agreed? |  |  | R |  |
| 34. | Has a vapour return line been connected? |  |  |  |  |
| 35. | If a vapour return line is connected, have operating parameters been agreed? |  |  |  |  |
| 36. | Are ship emergency fire control plans located externally? |  |  |  |  |

PART'A'- BULK LIQUID GENERAL (continued)

(This reproduction of Part A excludes questions 37/46 covering Crude Oil Washing and Inert Gas Systems)

If the ship is planning to tank clean alongside, the following questions should be answered.

| Tank Cleaning | Ship | Shore | Remarks |
| --- | --- | --- | --- |
| Are tank cleaning operations planned during the ship's stay alongside the shore installation? | Yes/No* |  |  |
| If so, have the port Authority and terminal authority been informed? | Yes/No* | Yes/No* |  |

* Delete Yes or No as appropriate

DECLARATION:

We the undersigned have checked, where appropriate jointly, the items on this check list and have satisfied ourselves that the entries we have made are correct to the best of our knowledge.

We have also made arrangements to carry out repetitive checks as necessary and agreed that those items with the letter 'R' in the column 'Code' should be re-checked at intervals not exceeding ___hours.

| For Ship | For Shore |
| --- | --- |
| Name: | Name: |
| Rank: | Position: |
| Signature: | Signature: |
| Date: Time: |